## Slide 1
Acoustics - disease detection
IMBALANCE-AWARE MULTI-DATASET LEARNING
July 23, 2026
NORTHWESTERN ENGINEERING

## Slide 2
Single-dataset learning is structurally long-tailed
2
NORTHWESTERN ENGINEERING
ICBHI 2017 • 6,898 cycles
SPRSound inter • 1,429 events
Normal
3642
Crackle
1864
Wheeze
886
Both
506
Normal
1040
Fine crackle
80
Coarse crackle
3
Wheeze
305
Wheeze + crackle
1
Aggregate performance can improve while rare-event learning still fails.

## Slide 3
Four datasets offer complementary—but non-identical—supervision
3
NORTHWESTERN ENGINEERING
ICBHI
920 recordings
6,898 cycles
Normal • crackle • wheeze • both
SPRSound
2,683 recordings
9,089 events
7 event types + record labels
HF_Lung
9,765 recordings
81,933 intervals
Breath phase + overlapping events
KAUH
336 recordings
112 patients
Recording sound type + diagnosis
Partial semantic overlap creates an opportunity for shared supervision
Crackle ↔ fine/coarse crackle • Wheeze ↔ wheeze • Other labels remain dataset-native
Recordings, cycles, events, and intervals are not interchangeable.

## Slide 4
Why naive pooling does not solve the problem
4
NORTHWESTERN ENGINEERING
NAIVE POOLING
Domain mismatch
Crackle, DAS, Crep, rhonchi and stridor are not automatically equivalent.
Sample-unit mismatch
Cycle, event, interval and recording labels supervise different targets.
Missing ≠ negative
Unlabeled HF background cannot be treated as Normal by default.
Dual imbalance
Large datasets and head classes can dominate the same objective.
Acquisition shortcut
Sampling rate, device, loudness and spectrum reveal dataset identity.
↘
↗
↗
↖
Paper contribution mut be a model / system / training strategy—not dataset aggregation.

## Slide 5
Acquisition fingerprints: loudness differs by ~26 dB
5
NORTHWESTERN ENGINEERING
LOUDNESS
ICBHI −16.8 dBFS SPRSound −43.2 dBFS
SNR PROXY
Medians span only 12.9–15.4 dB

## Slide 6
Raw spectral shape is strongly dataset-specific
6
NORTHWESTERN ENGINEERING
SPRSound concentrates energy in 100–250 Hz; HF_Lung is broader; ICBHI/KAUH are strongly low-frequency dominated.
These raw differences motivate harmonized preprocessing and dataset/device-stratified evaluation.

## Slide 7
Low-level acoustics identify the dataset with ~0.92–0.94 balanced accuracy
7
NORTHWESTERN ENGINEERING
Original plot
0.935 recording-level CV
Recheck
0.924 patient-grouped CV
SPRSound
336 / 336

## Slide 8
From source alignment to the open research question
8
NORTHWESTERN ENGINEERING
Patch-Mix
62.1708
author: 62.17
PAFA
64.143
paper: 64.84 ± 0.60
SG-SCL
60.984
paper: 61.71 ± 1.61
1
Source alignment
Verified
→
2
Direct source-head transfer
Verified
→
3
Frozen encoder + target head
Verified
→
4
Rare-event multi-dataset learning
Proposed

## Slide 9
Direct source decision layers do not transfer
9
NORTHWESTERN ENGINEERING
Same 1,429 SPRSound inter events
ZERO-TARGET-TUNING
Binary AS
Narrow-four diagnostic
Patch-Mix
59.38
51.15
PAFA
55.82
51.19
SG-SCL
59.98
50.08
Better than random guess
Source features may be useful; the source classifier is not.

## Slide 10
Frozen representations retain target-linear accessibility
10
NORTHWESTERN ENGINEERING
Binary AS on the same SPRSound inter set
ENCODER FROZEN
0
50
100
Patch-Mix
direct head 59.38
target head 87.68
PAFA
direct head 55.82
target head 84.29
SG-SCL
direct head 59.98
target head 90.65
the representation is reusable under target supervision.

## Slide 11
Aggregate recovery and minority failure coexist
11
NORTHWESTERN ENGINEERING
Seven-class aggregate metrics
SPRSound inter support
Patch-Mix
Official Score
82.37
Macro-F1
0.362
UAR
0.351
PAFA
Official Score
75.77
Macro-F1
0.387
UAR
0.279
SG-SCL
Official Score
84.41
Macro-F1
0.372
UAR
0.351
Normal
1040
Wheeze
305
Fine crackle
80
Coarse crackle
3
Wheeze + crackle
1
Wheeze + crackle recall = 0 for all three models

## Slide 12
Proposed system: share only acoustically compatible supervision
12
NORTHWESTERN ENGINEERING
ICBHI
→
SPRSound
→
HF_Lung
→
KAUH
→
OPTIONAL DATASET ADAPTERS
→
SHARED ACOUSTIC ENCODER
→
SHARED HEADS
crackle families • wheeze normal & abnormal
DATASET-NATIVE HEADS
quality / diagnosis / interval heads
dataset balancing × class balancing